## Slide 1: Alpha Satcom Waveguide Array Antennas PST 0.35 & 0.6-mtr Ku-band Portable Satcom Terminals
September 2022

## Slide 2: PST 0.35 & 0.6-mtr Ku-band Portable Satcom Terminals
The fully integrated, waveguide array antenna, is a compact design with LNB , BUC, Control board, Satellite Modem, Wireless Access Point and Battery contained in a single lightweight package.
Ultra Light and easily transportable, the Manual configuration weight is less than 8 kg, and the Auto-Pointing model is less than 12 kg.
After connecting with the antennas’ WiFi via a handheld device (IOS or Android) the GUI interface provides precise pointing to the satellite of interest.
Therefore the setup is a quick and easy operation, which is performed within 3 minutes by a single person without any tools.
Transport packaging is provided with a high strength, light weight aluminum-magnesium alloy case.

## Slide 3: PST .035 & 0.6-mtr Ku-band Portable Satcom Terminals
The ultra-light terminals are all-inclusive with built-in wireless design integrated with a satellite modem, WiFi Access Point, LNB/BUC, control logic board and battery.
The modem agnostic units currently have integrated devices such as iDirect and Gilat DVB/RCS modems.
The units are presently being used in emergency, public security, fire protection, meteorology, civil air defense, aerospace and military. industries.

## Slide 4: End-To-End Operational and Connectivity Overview
基站
HTS
0.35m Ku-band Terminal
Video conference
Video surveilance
VoIP Gateway
phone Fax
Stream Media
Internet
Mobile
BTS
Drone
Streaming media distribution terminal
Gateway

## Slide 5: 0.35-mtr Manual Ku-band terminal

## Slide 6: PST 0.35 & 0.6-mtr Ku-band Portable Satcom Terminals
Manual Auto Pointing
0.35m Satcom Terminal
0.6m Satcom Terminal
Manual Auto Pointing

## Slide 7: PST 0.35-mtr Ku-band Models
Auto Pointing Type
Manual Type

## Slide 8: Manual Configuration with WiFi Pointing Application

## Slide 9: Specifications of PST 0.35-mtr Antenna
Size | ≤L385mm*W315mm*H60mm | Weight | ≤6Kg(Manual） ≤8kg(Auto）
Input Power | 29.4V | Power Consumption | 110W
TX Freq Range | 14.0-14.5GHz | TX Gain | ≥32.5dBi
RX Freq Range | 10.7-12.75GHz | RX Gain | ≥31.5dBi
Pol | Linear | X-Pol Isolation | ≥30dB
G.T | ≥11dB/K | Equivalent aperture | ≥0.35m
Type | Waveguide Array Antenna | Max Power/EIRP | 16W/42dBm
Setup time | ≤3min | Satellite Acquisition | Manual/Auto Pointing
Battery Operation Time | ≥1.5 Hours |  | 
Protection Level | ≥IP67 |  | 
Altitude | ≥7200m |  | 

## Slide 10: PST 0.6-mtr Ku-band Portable Satcom Terminal
Manual Type
Auto Pointing Type

## Slide 11: PST 0.6-mtr Auto Pointing Ku-band terminal

## Slide 12: Specification of PST 0.6-mtr Antenna
Size | ≤ 95mm*370mm*60mm | Weight | ≤10kg (Manual） ≤12kg (Auto）
Input Power | 29.4V | Power Consumption | 110W
TX Freq Range | 14.0-14.5GHz | TX Gain | ≥36.8dBi
RX Freq Range | 10.7-12.75GHz | RX Gain | ≥35.6dBi
Pol | Linear | X-Pol Isolation | ≥30dB
G.T | ≥13dB/K | Equivalent aperture | ≥0.6m
Type | Waveguide Array Antenna | Max Power/EIRP | 16W/42dBm
Setup time | ≤3min | Satelllite Acquisition | Manual/Auto-pointing
Battery Operation Time | ≥ 2.5Hours |  | 
Protection Level | ≥ IP67 |  | 
Altitude | ≥ 7200m |  | 

## Slide 13: Auto-Pointing Pedestal

## Slide 14: Antenna Block Diagram and Layout
Waveguide Array Antenna
LNB
BUC
Modem card
Control Board
Power Supply
User Interface
M&C
WIFI
Battery

## Slide 15: Internal Space Available for Built-in Modem Card
BUC size：
Available 4W，8W，16W (in standard case) .
MAX 20-25W (larger cases)
Current Integrated Modem Types：
iDirect IQ200 modem card；
Gilat modem card；
Other satellite system modem cards can be integrated.
Max spaces for other modem cards
0.35-mtr antenna ：146*165*20 mm （W*L*H)
0.5 & 0.6-mtr Antenna ：292*330*40 mm

## Slide 16: Packing Weights & Dimensions
0.35m Antenna：49X41X37CM
Manual Type：
Net weight ≤6Kg；Gross weight: 10KG
Auto Type：
Net weight ≤8Kg；Gross weight: 12KG
0.6m Antenna: 65X35X45CM
Manual Type：
Net weight 8Kg；Gross weight：12.5KG
Auto Pointing Antenna：
  2 Boxes
  Box1：65X35X45CM
Box2：53X25X20.5CM
Net weight 12Kg； Gross Weight：17KG

## Slide 17: Backpack Configurations
PST 0.35-mtr Backpack
PST 0.6-mtr
Backpack

## Slide 18: Factory Staff & Production Capacity
Capacity production rate is, 100sets/month
Highly trained Engineering and Technical staff
Two production lines.
300 sets of test equipment

## Slide 19: Antenna Laboratory Test Equipment

## Slide 20: Product History
2017, Delivery of the first portable terminal, Ku-band Narrow band.
2019, Antenna Feeds were upgraded to operate at Wide Ku-band.
2021, Automatic pointing capability was added.
Audio pointing function for the manual system was added.
To date, more than 1000 Ku-band units have been delivered to emergency, public
security, fire protection, power grid, forest fire protection, and other critical
national and industrial organizations.
Currently manufacturing 100 sets of 0.5-mtr Ka-band system for a National
Satellite Operator.